### Integer serialization
191026, 26.10.2019/pekka
Serialization format is packed by integer value. Packed format is type and architecture independent , number of bytes generated depends only on value. Maximum integer size is 64 bits.

Bits in first byte byte NNNNSxxx:
- NNNN number of follower bytes.
- S sign, 0 for positive, 1 for negative.
- xxx Least significant 3 data bits.

Follower bytes hold the remaining data bits.

Required defines:
OSAL_SERIALIZE_SUPPORT = 1

Serializing an integer
The osal_intser_writer() function packs C integer x into buffer using serialization format. The function returns number of bytes written to the buffer.

os_int osal_intser_writer(
    os_char *buf,
    os_long x);

Reading an integer
The osal_intser_reader() function converts integer from serialization format into 64 bit C integer x.
The function returns number of bytes read from the buffer.

os_int osal_intser_reader(
    os_char *buf,
    os_long *x);